## Slide 1: Computer Architecture and Logic Design (CALD) Lecture 16
+

## Slide 2: Design Process of Synchronous Sequential Circuits

## Slide 3: Design Procedure
Design Procedure for sequential circuit
  The word description of the circuit behavior to get a state diagram;
  State reduction if necessary;
  Assign binary values to the states;
  Obtain the binary-coded state table;
  Choose the type of flip-flops;
  Derive the simplified flip-flop input equations and output equations;
  Draw the logic diagram;

## Slide 4: Design of Clocked Sequential Circuits
+
Example:
Detect 3 or more consecutive 1’s
S0 / 0
S1 / 0
S3 / 1
S2 / 0
0
1
1
0
0
1
0
1
State | A B
S0 | 0 0
S1 | 0 1
S2 | 1 0
S3 | 1 1

## Slide 5: Design of Clocked Sequential Circuits
+
Example:
Detect 3 or more consecutive 1’s
Present State |  |  |  | Input | Next State |  | Output
 | A | B |  | x | A | B | y
 | 0 | 0 |  | 0 | 0 0 |  | 0
 | 0 | 0 |  | 1 | 0 1 |  | 0
 | 0 | 1 |  | 0 | 0 0 |  | 0
 | 0 | 1 |  | 1 | 1 0 |  | 0
 | 1 | 0 |  | 0 | 0 0 |  | 0
 | 1 | 0 |  | 1 | 1 1 |  | 0
 | 1 | 1 |  | 0 | 0 0 |  | 1
 | 1 | 1 |  | 1 | 1 1 |  | 1
S0 / 0
S1 / 0
3
S / 1
2
S / 0
0
1
1
0
0
1
0
1

## Slide 6: Design of Clocked Sequential Circuits
+
Example:
Detect 3 or more consecutive 1’s
Present State |  | Input | Next State |  | Output
A | B | x | A | B | y
0 | 0 | 0 | 0 0 |  | 0
0 | 0 | 1 | 0 1 |  | 0
0 | 1 | 0 | 0 0 |  | 0
0 | 1 | 1 | 1 0 |  | 0
1 | 0 | 0 | 0 0 |  | 0
1 | 0 | 1 | 1 1 |  | 0
1 | 1 | 0 | 0 0 |  | 1
1 | 1 | 1 | 1 1 |  | 1
Synthesis using D Flip-Flops
A(t+1) = DA (A, B, x)
= ∑ (3, 5, 7)
B(t+1) = DB (A, B, x)
= ∑ (1, 5, 7)
y (A, B, x) = ∑ (6, 7)

## Slide 7: Design of Clocked Sequential Circuits
+
DA (A, B, x) = ∑ (3, 5, 7)
= A x + B x DB (A, B, x) = ∑ (1, 5, 7)
= A x + B’ x
y (A, B, x) = ∑ (6, 7)
with D F.F.
Example:
Detect 3 or more consecutive 1’s
Synthesis using D Flip-Flops
B
 | 0 | 0 | 1 | 0
A | 0 | 1 | 1 | 0
 |  | x |  | 
B
 | 0 | 1 | 0 | 0
A | 0 | 1 | 1 | 0
 |  | x |  | 
B
 | 0 | 0 | 0 | 0
A | 0 | 0 | 1 | 1
 |  | x |  | 
= A B
Eastern Mediterranean University

## Slide 8: Design of Clocked Sequential
+
DA = A x + B x DB = A x + B’ x y = A B
Circuits with D F.F.
Example:
Detect 3 or more consecutive 1’s
Synthesis using D Flip-Flops
D Q
Q
A
CLK
x
B
D Q
Q
y

## Slide 9: Flip-Flop Excitation Tables
+
Present State | Next State | F.F. Input | 
Q(t) | Q(t+1) | J | K
0 | 0 | 0 x | 
0 | 1 | 1 x | 
1 | 0 | x 1 | 
1 | 1 | x 0 | 
Present State | Next State | F.F. Input
Q(t) | Q(t+1) | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
0 0 (No change)
1 (Reset)
0 (Set)
1 1 (Toggle)
1 (Reset)
1 (Toggle)
0 (No change)
0 (Set)
Q(t) | Q(t+1) | T
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 10: Design of Clocked Sequential
+
Circuits with JK F.F.
Example:
Detect 3 or more consecutive 1’s
Present State |  | Input | Next State |  | Flip-Flop Inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 | 0 | 0 | 0 x |  | 0 x | 
0 | 0 | 1 | 0 | 1 | 0 x |  | 1 x | 
0 | 1 | 0 | 0 | 0 | 0 x |  | x 1 | 
0 | 1 | 1 | 1 | 0 | 1 x |  | x 1 | 
1 | 0 | 0 | 0 | 0 | x 1 |  | 0 x | 
1 | 0 | 1 | 1 | 1 | x 0 |  | 1 x | 
1 | 1 | 0 | 0 | 0 | x 1 |  | x 1 | 
1 | 1 | 1 | 1 | 1 | x 0 |  | x 0 | 
Synthesis using JK F.F.
JA (A, B, x) = ∑ (3)
dJA (A, B, x) = ∑ (4,5,6,7)
KA (A, B, x) = ∑ (4, 6)
dKA (A, B, x) = ∑ (0,1,2,3)
JB (A, B, x) = ∑ (1, 5)
dJB (A, B, x) = ∑ (2,3,6,7)
KB (A, B, x) = ∑ (2, 3, 6)
dKB (A, B, x) = ∑ (0,1,4,5)

## Slide 11: Design of Clocked Sequential
+
Ea
stern Mediterranean University
JA = B x JB = x
KA = x’
KB = A’ + x’
Circuits with JK F.F.
Example:
Detect 3 or more consecutive 1’s
Synthesis using JK Flip-Flops
B
 | 0 | 0 | 1 | 0
A | x | x | x | x
 |  | x |  | 
B
 | x | x | x | x
A | 1 | 0 | 0 | 1
 |  | x |  | 
B
 | 0 | 1 | x | x
A | 0 | 1 | x | x
 |  | x |  | 
B
 | x | x | 1 | 1
A | x | x | 0 | 1
 |  | x |  | 
CLK
J Q
K Q
x
A
B
J Q
K Q
y

## Slide 12: Design of Clocked Sequential
+
Present State |  | Input | Next State |  | F.F. Input | 
A | B | x | A | B | TA TB | 
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0
Circuits with T F.F.
Example:
Detect 3 or more consecutive 1’s
Synthesis using T Flip-Flops
TA (A, B, x) = ∑ (3, 4, 6)
TB (A, B, x) = ∑ (1, 2, 3, 5, 6)

## Slide 13: Design of Clocked Sequential
+
TA = A x’ + A’ B x TB = A’ B + B  x
Circuits with T F.F.
Example:
Detect 3 or more consecutive 1’s
Synthesis using T Flip-Flops
B
 | 0 |  | 0 | 1 | 0
A | 1 |  | 0 | 0 | 1
 |  |  | x |  | 
B
 | 0 | 1 | 1 | 1
A | 0 | 1 | 0 | 1
 |  | x |  | 
A
B
y
T Q
Q
x
T Q
Q
CLK